## Slide 1
Ossy Siegmund,
Experimental Astrophysics Group,
Space Sciences Laboratory,
U. California at Berkeley
20cm Sealed Tube Facility at SSL

## Slide 2: 8” Sealed Tube Resources at SSL
SPECIFIC FACILITY SAMPLE SIZE LARGE 8.6” SIZE
Precision Wet Cleaning In Service In Service
Vacuum Baking In Service In Assembly
N2 & Vacuum Storage In Service In Service
Hi-Pot Station In Service In Service
Plasma Cleaning In Service In Service
Helium Leak Checker In Service Use RGA
Electrode Evaporation In Service In Service
1.2” PC Process Chamber In Service
8.6” Cathode/seal/test Chamber Commissioned
8.6” Full Process Chamber In final assembly

## Slide 3
3
Plasma Etcher
Plasma etcher commissioned
Vital for cleaning windows.
Has been tested with, oxygen, argon and hydrogen gases.

## Slide 4: Evaporator accommodates 8.7” windows
In operation for NiCr/Cu evaporation tooling for 8.7” windows

## Slide 5: Large Vacuum Bake Chamber
Use for tube assembly pre-bake
To be used for parts preconditioning
Stand ready
Have base flange, needs mods
Heaters and insulation spec’d
Thermal control system spec’d
Will get on short turnaround
finish assembly and commission.

## Slide 6
Precision Wet Cleaning
Ultrasonic, chemicals, oven, DI etc available
Wet cleaning station
Jig for window/MCP wet cleaning

## Slide 7: Large Process Chamber Design
Detector Body Stack on 16.5” CF Flange
Multiple Viewports
8” P-C Forming Well Tube
Vacuum Chamber 18” O.D x 30” Long
Multi- Motion Manipulator Arms
All-Metal Valves to Three Pumping Ports
Two UHV Ion Pumps
14” Access Tube

## Slide 8: Large Process Chamber
Chamber Construction.
Chamber on process cart with:-
Viewports
Tube support flange
Loading jack
two ion pumps,
Pump controllers
Alkali sources

## Slide 9: Large Process Chamber
Chamber on process cart with:-
Support/translation ports
Oven base support/insulator
Half of insulator support base
Alkali power leads
Base frame with rollers

## Slide 10
10
Oven for Test/Process Station.
Oven accommodates Large Format Inside Envelope: 36” x 30” x 25” High
Defines Large Chamber Limits
Cathode station controls alkali metal deposition, and monitors cathode response

## Slide 11
11
Tube Test/Process Station.
Large tube station replaces existing process station
Use existing:-
Electrometer for cathode signal.
Power controls for alkalis.
Monochromatic LED’s
for response measurements.
NIST photodiodes for QE test.
Need:-
RGA for gas monitoring.
Large turbo/scroll station for servicing/bakeout support.

## Slide 12: Large Process Chamber
Ion pump ports
Manipulator ports
Rough port
RGA port
Need to finish internal fixtures:- transport, covers, forming well