10 GS/s sampling chip minimum specifications.

Sampling rate              10GS/s

Analog Bandwidth      2GHz

Dynamic range            0.7V

Number of channels    4

Number of samples     256

Sampling window       adjustable 500ps-2ns

Sampling jitter            10ps

ADC Resolution         8-bit (12-bit implemented)

LSB                             0.17 mV

Crosstalk                     1%

DC Input impedance   50 internal (channels 0 and 1)

Write clock                 40 MHz

Read clock                  40 MHz

Conversion clock        adjustable 1-2 GHz internal ring oscillator

Readout time               4 x 256 x 25ns=25.6 s

Power                          40mW/channel

Power supply              1.2V

Process                        IBM 8RF-DM (130nm CMOS)